## Slide 1
Carbon monoxide monitoring as a motivational tool
Notes: Carbon monoxide testing as a motivational tool
We are now going to look in more detail at carbon monoxide monitoring and its role as a motivational tool.

## Slide 2
CO is a poisonous gas produced by smoking tobacco
It affects the body’s ability to transport oxygen, reducing the oxygen available
It is responsible for much of the harm to health
caused by smoking
Carbon monoxide
Inpatient Tobacco Dependence Treatment Training Programme
Notes: CO is a poisonous gas contained in cigarette smoke; it affects the body’s ability to transport oxygen around the body.
CO is absorbed into the blood from the lungs. It binds to haemoglobin in red blood cells about 200 times as readily as oxygen. CO deprives the body of oxygen which the body needs to survive.
The tar, carbon monoxide and toxins in tobacco smoke is what causes harm and leads to smoking-related illness.

## Slide 3: Carbon monoxide monitoring
CO monitors measure the amount of ​ carbon monoxide in expired breath, displayed as parts per million (ppm) ​
CO monitors detect exposure to smoke ​ in the previous 24 – 48 hours​
Motivational tool, chart progress​
Notes: CO monitors measure the amount of carbon monoxide in expired breath, displayed as parts per million (ppm)
CO monitors detect exposure to smoke in the previous 24 – 48 hours
Motivational tool, chart progress, by providing with personalized feedback on their smoking, but also immediate benefits of stopping on their body, recovery, and health
There are a number of CO monitors available and you should follow the instruction accompanying these machines, and local infection control procedures. These actions are fairly common to all monitors however.
Infection control
Mouthpiece is for single use only
Dispose of mouthpiece by asking patient to remove and immediately throw into bin
Change ‘D’ piece as per instructions (this is the one-way bacteria filter)
Use recommended compatible wipes
Use of alcohol wipes can affect the electrochemical sensors
  Can cause permanent damage
  Affect reading giving false positive/negative readings

## Slide 4: CO Monitoring Demonstration
Appendix 8
Patients are required to hold their breath for 15 seconds (minimum 10 seconds) to equalise pressure in the lungs and allow CO to transfer between blood and lungs​
CO monitoring demonstration
Inpatient Tobacco Dependence Treatment Training Programme
Notes: CO testing Demonstration
We will briefly demonstrate how to conduct a CO test with patients. There are a variety of devices available but they all essentially work in the same way.
For patients who suffer from anxiety, you will want to be conscious to explain the test slowly, allow them to take their time and conduct the test when they feel comfortable doing so (possibly later in the session) or at the next session.
A – VIRTUAL COURSE:
Option 1: Live demonstration
Equipment needed: CO monitor, disposable tubes, non-alcoholic wipes.
Trainer demonstrates how the device is used by conducting test on themselves. Demonstrate:
How to turn it on
How to insert mouthpiece
How to start test
Take deep breath (hold for 15 seconds while monitor counts down)
Monitor beeps last 3 seconds, pass to the patient
Advise patient to exhale slowly, aiming to empty their lungs of air
Show where the result is displayed on the monitor
Dispose of monitor
Brief review of infection control practices (patient inserts and removes tube and disposes of safely)
Option 2: Film Clip
The video clip we are about to watch provides a demonstration on how CO testing is conducted.
[Play video: https://elearning.ncsct.co.uk/vbaplus_homelessness-stage_29]
After the video highlight the following:
Hold breath for 15 seconds
Need for the tight seal
Show patient their reading
You may wish to show a CO reading chart to patients (in particular those reducing to quit)
Mention infection control practices (patient inserts and removes tube and disposes of safely). Note that this is not included in film clip.
B – FACE-TO-FACE COURSE:
Live demonstration
Equipment needed: CO monitor, disposable tubes, non-alcoholic wipes.
One trainer playing role of patient and the other the practitioner. Repeat the above instructions for trainer demonstration.
Participant CO-testing practice skills:
Equipment needed: Multiple CO monitors (ideally 4-5), disposable tubes (for each participant or half of group).
Participants who have not previously used a monitor are offered the opportunity to use the device on themselves or another participant.
Protocols should be followed for cleaning the device (i.e. new tube for each person, tube disposed of by individual, device cleaned with non-alcoholic wipe between tests).
Use recommended compatible wipes
Use of alcohol wipes can affect the electrochemical sensors, can cause permanent damage and affect the reading by giving false positive/negative readings.
Before the test
When introducing the test to patients it can be helpful to explain how the test works:
“This machine measures the amount of carbon monoxide in your lungs in parts per million. Carbon monoxide is a poisonous gas inhaled by people who smoke cigarettes and it causes heart disease and other serious health issues. This CO test will give us an indication of how much carbon monoxide is circulating in your body. It provides you will with visible proof of the harm smoking is doing to your body.”
After the test
“The monitor is showing a reading of [X]. The normal range for a non-smoker (person who does not smoke) is between 1 and 5 ppm and so you can see that your reading is [X times or much] higher much than the normal healthy levels. The good news is that when you get to the point of stopping completely this will quickly come down to the levels of a healthy non-smoker. This is a nice way for us to see the benefits of stopping smoking on your health. We will repeat the test each week but would expect the reading to be over 5ppm until you stop completely.”
CO has a relatively short half-life (4 hours) and is eliminated fairly quickly from the bodies of smokers and therefore CO monitors can only tell us about recent exposure to tobacco smoke and not whether someone is a smoker or not.
For CO screening to be conducted properly, patients must hold their breath for 15 seconds before blowing into the CO monitor; this allows time for the CO in the blood to pass into the air in the lungs.
CO is used as a tool for validation but it is equally important as a motivational tool as it allows the patient to see objective proof of toxins leaving the body.

## Slide 5: Discussing results with patients
Appendix 9
The test results should be recorded in the patients ​notes
0 – 6 ppm
Typical levels for a non-smoker, and should be your goal.
It is normal to have some CO in your body.
7 – 9 ppm
Borderline values that may be found in smokers and non-smokers.
10+ ppm
Typical levels for a smoker.
Notes: Test results should be shared with patients, in the context of increasing their interest in stopping smoking.
Many of you may have seen these CO charts. You can find a copy of a CO chart in Appendix 9 or the STP. This chart can be a useful tool for sharing CO test results with patients.
Importantly, because CO monitors can only measure CO from exposure to smoking within 24 -48 hours, you will want to place that in context with patients.
When a series of test results are available to view, the patient and TDA should reflect together to see if there are any patterns which might help further strengthen the care plan.
The test results should be recorded in the patients notes and discussed in the clinical review meetings.

## Slide 6
What can affect carbon monoxide readings?
Inpatient Tobacco Dependence Treatment Training Programme
Notes: [Ask participants to note via the chat function what they know of that may affect CO readings]
If the patient has smoked immediately prior to the test, the CO readings will be higher, than those who smoked hours earlier (possibly not being able to smoke due to their condition or smokefree environment)
Consider how representative is it of their normal smoking pattern? e.g. have they just had a cigarette or not yet smoked that day?
Recordings in the afternoon are probably the best for consistency.
Machines should be calibrated regularly (once a year).
Secondhand smoke
Passive exposure to tobacco smoke would need to be extremely heavy to alter the CO reading by >2–3 ppm
Lactose intolerance
Sensors in monitors are sensitive to hydrogen
Hydrogen is naturally produced in the gut (normally in low concentrations)
Any intolerance to sugars such as lactose or fructose produce higher levels

## Slide 7: Summary
Creates a dialogue with the patient, allowing you to explain how smoking affects their health and recovery
Motivates to make a quit attempt or remain smokefree
Provides patients with personalised feedback (their measurement) to allow them to make an informed decision
CO is eliminated very quickly, therefore positive effects of not smoking can be seen immediately
Inpatient Tobacco Dependence Treatment Training Programme
Notes: [read through list]